## Slide 1
RECOLIFT: AN ANDROID WEAR FITNESS TRACKER FOR STRENGTH TRAINING
Dario Aranguiz
Advisor: Professor Romit Roy Choudhury
May 6, 2015
Notes: ECE Main Slide

## Slide 2
Pictured: Dan Green, jtsstrength.com
MOTIVATION
How do you marry interests in lifting, mobile, and DSP?
A few thoughts:
1.5 million Apple Watches sold in two weeks
Almost 1 million Android Wear devices sold in 2014
Apple, Google creating health APIs
Few strength-training devices on market

## Slide 3
Pictured: Sony Smartwatch, http://www-static.se-mc.com
THE END GOAL
To create an application which:
Tracks lift types, sets, and reps
Requires no user input
Uses off-the-shelf hardware

## Slide 4
CHALLENGES
Segmenting exercise from non-exercise
Recognizing which lift is being performed
Counting repetitions with a noisy signal
Curl Accelerometer
Data
Squat Accelerometer
Data

## Slide 5
PREPROCESSING
Resample
  25Hz Zero Order Hold
Low pass filter
  12Hz 5th Order Butterworth
Compute new signals
  Magnitude
  Projection onto PCA axis
Pictured: PCA example, weigend.com

## Slide 6
SEGMENTATION - FUNDAMENTALS
Primary intuition
  Exercise is periodic
  Non-exercise is aperiodic
Curl Accelerometer
Data
Idling Accelerometer
Data

## Slide 7
SEGMENTATION - PROCESS
Compute signal autocorrelation
Extract features
Classify with SVM
  Majority vote

## Slide 8
SEGMENTATION - AUTOCORRELATION

## Slide 9
RECOGNITION
Extract features
  Autocorrelation
  Mean, Standard Deviation, etc
Classify with SVM
Curl Accelerometer
Data
Squat Accelerometer
Data

## Slide 10
COUNTING – ALGORITHM (1)
Find all local maxima
  Constrained to some minimum period between peaks

## Slide 11
COUNTING – ALGORITHM (2)
Perform autocorrelation around each peak
  Determine local period
  Cull any peaks that occur too close

## Slide 12
COUNTING – ALGORITHM (3)
Find peak at 40th percentile
  Cull all peaks less than 50% of that peak

## Slide 13
RESULTS
Battery Drain: ~10% per hour
Accuracy: Need more training data
Current supported lifts:
Bench Press
Overhead Press
Squat
Preacher Curl
Pendlay Row
Soon:
Deadlift
Lat Pulldown
Shoulder Fly